|  | 8 Port IP KVM |
| --- | --- |
|  | Model: DKVM-IP8 Console Management at Anywhere & Anytime |

DKVM-IP8 defines a new class of remote KVM access device; it combines digital remote KVM access via IP networks with comprehensive and integrated system management.

DKVM-IP8 owes a convenient, remote KVM access and control via LAN or Internet. It captures, digitizes, and compresses video and transmits it with keyboard and mouse signals to and from a remote computer. Also it provides a non-intrusive solution for remote access and control. Remote access and control software runs on its embedded processors only but not on mission-critical servers, so that there is no interference with server operation or impact on network performance.

※ Features

- Manage multiple serves around the world.

- Built in 8 ports KVM.

- KVM access over IP, ISDN or analogous telephone line.

- BIOS level access.

- Virtual Storage Mapping.

- SSL encryption.

- No impact on server or network performance.

- Automatically senses video resolution for best possible screen capture.

- High-performance mouse tracking and synchronization.

※ Package contents

- DKVM-IP8*1

- QIG (Quick Installation Guide)

- User Manual on CD-ROM*1

- Cables:

- 1-to-3 console cable (1.8M)*2

- Daisy-chain cable (0.9M)*1

- LAN Cable*1

- USB Cable (A-B)*1

- Null modem cable*1

- Power Adapter*1 (5V, 2.5A)

- Rack Mount Kit*1

- Diagram

※ Specification

| Specification | DKVM-IP8 |
| --- | --- |
| PC Connection | Direct | 8 |
|  | Max. via Daisy Chain | 120 (8 port + 16 port * 7 levels) |
| Port Selection | Push button, Hotkey, OSD |
| Connectors | Console | Keyboard | 1*Mini Din 6 Female (Purple) |
|  |  | Video | 1*HDB15 Female (Blue) |
|  |  | Mouse | 1*Mini Din 6 Female (Green) |
|  | Computer | 8*SPHD 15 pin Female (Blue) |
|  | Daisy Chain | Keyboard | 1*Mini Din 6 Female (Purple) |
|  |  | Video | 1*HDB15 Female (Blue) |
|  |  | Mouse | 1*Mini Din 6 Female (Green) |
|  | Serial Port | 1*DB9 pin Male |
|  | USB Port | 1*USB 2.0 Type B |
|  | LAN | 1*RJ-45 Female |
|  | Power | 1*DC Jack (Black) |
| Emulation | Keyboard / Mouse | PS/2 |
| LED | Online | 8 |
|  | 10 / 100 Mbps | 1 (Orange / Green) |
|  | 7-Segment | 1 |
| Scan Intervals | 5~99 Sec |
| Reset button | 1 |
| VGA Resolution | Local: 1600*1200 Remote: 1280*1024 |
| Environment | Operation Temperature | 0 ~ 5°C |
|  | Storage Temperature | -20 ~ 60°C |
|  | Humidity | 0 ~ 80%, Non-Condensing |
| Power Adapter | DC 5V, 2.5A |
| Physical Properties | Housing | Metal |
|  | Weight | 2,600g |
|  | Dimensions (L*W*H), mm | 44*430*220 |