## Slide 1
D-Link Business Wireless LAN Solution

## Slide 2: D-Link Unified Wireless Solution
Wireless controller
Unified switch
DWC-1000
Support 6~24 APs per device
Support 24~96 APs per peer group
DWS-4026
Support 64 APs per device
Support 256 APs per peer group
DWS-3160
Support 12~48 APs per device
Support 48~192 APs per peer group
DWC-2000
Support 64~256 APs per device
Support 256~1024 APs per peer group
NEW

## Slide 3: Unified Wireless Solution Comparison
 | DWC-1000 | DWS-3160 | DWS-4026 | DWC-2000
Port | 4LAN+ 2Option 10/100/1000Based-T | 20 10/100/1000Base-T 4 Combo 1000 Base-T/SFP | 24 10/100/1000Base-T 4 Combo 1000 Base-T/SFP 2 10G (module/ optional) | 4 10/100/1000Base-T 4 Combo 100/1000 Base-T/SFP
PoE | No | Yes (PC model) | Yes | No
# mgmt. AP | 6 to 24 | 12 to 48 | 64 | 64 to 256
Max. # mgmt. AP/ peer group | 96 | 192 | 256 | 1,024
# clustering controller/ peer group | 4 | 4 | 8 | 8
Redundancy while full AP capacity | No | No | Yes (4+4) | Yes (4+4)
Additional VPN/ Firewall/ WCF license | Yes | No | No | No
Additional AP license increments | 6 | 12 or 24 | No | 32 or 64 or 128
v
v

## Slide 4: Wireless Controller License Options
DWC-1000
DLMS* Virtual Pack
*Remark:
DLMS, D-Link License Management System , an on-line system delivering virtual package of appliance’s add-on services, instead of physical one.
DWC-2000
AP License
  To activate an additional 6 access points
  DWC-1000-AP6/ DWC-1000-AP6-LIC
Feature license (DWC-1000-VPN-LIC)
  To activate VPN, firewall and advanced routing features
  DWC-1000-VPN/ DWC-1000-VPN-LIC
AP License
  To activate additional access point support
  DWC-2000-AP32/ DWC-2000-AP32-LIC
  DWC-2000-AP64/ DWC-2000-AP64-LIC
  DWC-2000-AP128/ DWC-2000-AP128-LIC

## Slide 5: Unified Wireless Access Point
DWL-8600AP
11n concurrent dual band
2 x 2 antennas
802.3af PoE
DWL-6600AP
11n concurrent dual band
Internal PIFA antennas w/ external antenna connectors
802.3af PoE
DWL-3600AP
11n 2.4GHz single band
Internal 2 x 2 antennas
802.3af PoE
DWL-8610AP
11ac concurrent dual band
Internal 3 x 3 antennas
802.3at PoE
DWL-2600AP
11n 2.4GHz single band
Internal 2 x 2 antennas
802.3af PoE
DWL-6610AP
11ac concurrent dual band internal 2x2 antennas
802.3at PoE
DWL-6700AP
Outdoor
11n concurrent dual band
2 x 2 antennas
5GHz high gain directional
2.4GHz omni-directional
Non-standard PoE
IP65 rated

## Slide 6: DWL-6700 Outdoor AP

## Slide 7: Unified Wireless Access Point 802.11ac AP
The first unified AP 802.11ac model.
3x3 MIMO with 3 spatial streams, providing up to 1300 Mbps PHY data rate on the 5GHz interface
POE: IEEE 802.3at
Bandsteering
Beamforming technology enables longer reach, thus covering more area with less devices
16 VAPs
AP Clustering
DWL-8610AP
11ac concurrent dual band
Internal 3 x 3 antennas
802.3af PoE
NEW
300
Mbps
450 Mbps
1300 Mbps

## Slide 8
DWC-2000

## Slide 9: DWC-2000 Form Factor
A | Reset button
B | Power LED
C | Fan LED
D | USB Ports (1-2)
E | Hard Disk Drive Module Slot
F | Gigabit LAN SFP ports (1-4)
G | Gigabit LAN RJ-45 ports (1-4)
H | Console Port
Interface
A
B
C
D
E
F
G
H
Link Aggregation
LACP

## Slide 10: DWC-2000 vs. DWC-1000
In addition to hardware (capacity, form factor…), software features and license options, there is one significant difference between Ethernet interfaces:

## Slide 11: DWC-2000 Highlight
System Performance
  64 APs per controller, max. 256 APs
  Max. 1,024 APs per peer group
  Max. 8 controllers per peer group ( including redundant controllers)
  Max. 3,072 concurrent CP authentication users
User Authentication
  20K permanent accounts and 20K temporary accounts of local database
  Multiple login pages associated with VLANs/ SSIDs
Hotspot Application
  Single or batch accounts generation
  Customized time/ traffic accounting profile
  User account status monitoring
  User account usage extension
  Payment agent (Paypal, SecurePay, Authorize.net, WorldPay)

## Slide 12: Hotspot Application Guest Management
Account generation from Service Desk/ Front Desk or via online purchasing*.
Up to 40 billing plans
Single or batch accounts creation
Flexible account type sorted by usage volume, usage time, and specific period.
Monitor status and extend usage via front desk account
Account usage status
Extend account usage and detail info
Batch generation
Billing plan selection
* Online purchasing: confirm with PP for supporting in your countries.

## Slide 13: Hotspot Application Payment Gateway
Purchase the wireless service online! Customer simply picks, chooses and purchases the wireless service on his tips.
Include most popular payment gateways ( e-commerce application service providers): PayPal, Secure Pay, WorldPay, and Authorize.net.
Benefits: leverage payment gateways’ infrastructures
  Collect funds cross countries and regions worldwide
  Secure transaction, encryption
Internet
Firewall
Switch
DWC
UAP
End Device
Customer
1
2
3, 4, 5
9
10
11
6
8
7
[Usage Scenario]
Wireless clients associate UAP
User opens a browser
DWC redirects to service package list
User chooses service package
User fills out payment gateway account (ex. Paypal) or credit card information
DWC passes credit card information to the payment gateway
The payment gateway validates transaction information
The payment gateway confirms the transation information to DWC
DWC generates a user account
DWC passes the qualified user account to the UAP
User acquires the internet access

## Slide 14: Hotspot Application Multiple Login Pages
Separate welcome pages assigned to different SSIDs or VLANs allow each company or service provider to have their own login portals, even if access points are managed by the same wireless controller.
Max. 10 login pages
SSID: AAA
Commercial Building
Company A
Company B
SSID: BBB
Internet
DWC

## Slide 15: DWC-2000 User Interface
The dashboard gives a quick glance on system, wireless and clients information
Traffic information is displayed neatly in a table.
Step-by-step instruction guides users to setup the system in minutes.
Main menu bar makes it easy to navigate among configurations

## Slide 16: DWC-2000 GUI Tips
Status is highlighted in color
Right-click on PC or long tap on touch panel on tablet to get a pop-out option list
Table content key word search
Sorting info by category
System function key word search

## Slide 17: DWC-2000 GUI Tips
Always think of “search” and “right-click” when you get lost.

## Slide 18: Getting Start
Avoid jumping into configuration directly without a proper plan.
Before starting configuration, make sure the following information is ready:
  IP plan
  VLAN plan
  Network topology
  Wireless features you would like to configure, including
    Country
    SSID
    Radio
    Wireless security
    …more

## Slide 19: Configure LAN Settings

## Slide 20: Discover Access Points(1/2)

## Slide 21: Discover Access Points(2/2)

## Slide 22: Manage Access Points(1/6)

## Slide 23: Manage Access Points(2/6)

## Slide 24: Manage Access Points(3/6)

## Slide 25: Manage Access Points(4/6)

## Slide 26: Manage Access Points(5/6)

## Slide 27: Manage Access Points(6/6) The power of search

## Slide 28: Add an AP Profile(1/5)

## Slide 29: Add an AP Profile(2/5)

## Slide 30: Add an AP Profile(3/5)
Turn on 5GHz radio
Select radio mode
Turn on auto-channel and auto-power
Remember to click “Save”
* Please note that values need to be given to all blank field.

## Slide 31: Add an AP Profile(4/5)
The newly created profile shows up in the “AP Profiles” list.

## Slide 32: Add an AP Profile(5/5)
After the profile is created, it will show up in the profile list where it can be applied.

## Slide 33: LAB 1: Use DWC-2000 to Manage APs
LAB Objectives: at the end of the lab, you will be able to use DWC-2000 to manage access points by applying a customized profile.
Tasks:
Configure the controller
Discover access points
Manage access points
Create an AP profile
Create a SSID named DEU-0x, where x stands for the group number. Use WPA2-personal, passcode: dlink123 as the security profile
Apply the AP profile to the access point
Associate to the SSID using your wireless clients
Raise your hand and tell me to verify it.
DWC-2000 IP: 192.168.10.5/24

## Slide 34: AP Profile SSID Setting(1/7)
You can select option to add a new SSID profile or modify the default SSID from the SSID profile list.

## Slide 35: AP Profile SSID Setting(2/7)
Right click any of the 16 default SSIDs you would like to edit.

## Slide 36: AP Profile SSID Setting(3/7)

## Slide 37: AP Profile SSID Setting(4/7)
Or you can experience the power of search again!

## Slide 38: AP Profile SSID Setting(5/7)

## Slide 39: AP Profile SSID Setting(6/7)

## Slide 40: AP Profile SSID Setting(7/7)

## Slide 41: Associated Wireless Clients
iPhone and the laptop wireless clients connect to GOA-1 SSID
Right click client to view more information

## Slide 42: Associated Wireless Clients Actions

## Slide 43: Scenario: separate and grant different privileges to company and personal devices
Description: Nowadays it’s very common for people to have multiple wireless devices, which are carried by employees to their company. A common policy of company IT team: your own device could only connect to the Internet whereas company devices could connect to both the Internet and the company resource.
Tasks:
Configure network infrastructure
Create company and BYOD VLANs
Create AP profiles and SSIDs
Configure captive portal for SSIDs
Create company user accounts
Add company device’s MAC address
Change AP’s profile to BYOD profile
Create and customize login profiles
Create captive portal accounts
Connect to both SSIDs
Verify the result
Internet
Company devices
Company Resource
Full
Internet only
YOD (Your Own Device)

## Slide 44: Configure switches and gateway
Internet
SSID1: company0x
SSID2: byod0x x stands for the group number
VLAN | Name | IP (DSR) | IP (DWC-2000)
1 |  | 192.168.10.1 | 192.168.10.5
2 | v2 | 192.168.2.1 | 192.168.2.5
3 | v3 | 192.168.3.1 | 192.168.3.5
a
b
c
d
e
f
a. Port 1/trunk/ VLAN 1, 2, 3
b. Port 1/Tagged, VLAN 2, 3 /untagged VLAN1
c. Port 2/Tagged, VLAN 2, 3 /untagged VLAN1
d. Port 3/Tagged, VLAN 2, 3 /untagged VLAN1
e. Port 10/untagged/ VLAN 2
f. Port 4/Trunk/ VLAN 1, 2, 3
DWC
DSR
DGS
* Disable DSR wireless if any

## Slide 45: Create VLANs on DWC(1/3)
Add VLANs

## Slide 46: Create VLANs on DWC(2/3)
You are allowed to configure IP address during VLAN creation in new GUI.
You are also allowed to configure DHCP on the same page in the new GUI.

## Slide 47: Create VLANs on DWC(3/3)
Verify your settings

## Slide 48: Configure Port Property as Trunk

## Slide 49: Create SSIDs(1/2)
Create 2 SSIDs: company0x and byod01 where x stands for group number.
MAC authentication is required for company0x SSID
SSID | company0x | byod0x
VLAN | 2 | 3
MAC Auth | Local | Default

## Slide 50: Create SSIDs(2/2)
Verify your settings

## Slide 51: Create an AP Profile(1/2)
Create an AP profile named BYOD, accepting any AP hardware type.

## Slide 52: Create an AP Profile(2/2)
Change profile SSID setting for both radios.
Remember to enable the 2nd SSID.

## Slide 53: Apply AP Profile to the AP
Apply the profile to the selected AP in Valid AP list if the access point is managed.
If access points are not managed, discover and manage them. You can assign the AP profile during AP management process.

## Slide 54: Create CP User Account(1/2)

## Slide 55: Create CP User Account(2/2)
Create a user name “user01” with a password “user01”

## Slide 56: Add Company Device MAC

## Slide 57: Connect Devices(1/3)
Connect company-owned devices to the company01.
Typing any valid IP, you will be redirected to company device portal.
Your own device could not connect to this SSID.

## Slide 58: Connect Devices(2/3)
Your own device could only connect to byod01 SSID.
It is only allowed to connect to the Internet

## Slide 59: Connect Devices(3/3)
You can verify the captive portal session from the “Captive Portal Session List” under Status  Network Information

## Slide 60: LAB: separate and grant different privileges to company and personal devices
LAB time: 40 minutes
You need to finish all the tasks in order to separate company and personal devices and grant different privileges to those devices
Internet
Company devices
Company Resource
Full
Internet only
YOD (Your Own Device)

## Slide 61: Scenario: Guest Management
Description: Nowadays it’s very common for company receptionists, hotspot managers, hotel front desk staff…etc. to manage visitors’ network access. This requirement can be carried out through DWC-2000 guest management function.
Tasks:
Create guest SSIDs
Create a front desk user
Create billing profile(s)
Login as a front desk and generate guest accounts
Test generated accounts

## Slide 62: Guest Management
Create a SSID for hotel guests

## Slide 63: Guest Management
Apply the SSID to both of the radios to the existing AP profile

## Slide 64: Guest Management
Enable the SSID
Reapply the AP profile to access points

## Slide 65: Guest Management
Create front desk accounts
Create a group for the front desk account in the first place.
Select “Front Desk” as the user type

## Slide 66: Guest Management
Create accounts for the guest management group.

## Slide 67: Guest Management
Create a billing profile for passcode generation.

## Slide 68: Guest Management Hotel Scenario(1/9)
The usage scenario: One of our hotel customer would like to have their front desk staff to generate temporary Internet access accounts for their hotel guests.
The front desk staff is able to generate 10 codes at once.
The hotel gives their guests 24 hours complimentary wireless access for 2 devices after their first login.

## Slide 69: Guest Management Hotel Scenario(2/9)
Sign in as a front desk to manage guest pass codes

## Slide 70: Guest Management Hotel Scenario(3/9)
From here, the front desk staff could generate codes and view codes information.

## Slide 71: Guest Management Hotel Scenario(4/9)
One code is generate; the front desk staff could print it.

## Slide 72: Guest Management Hotel Scenario(5/9)
The front desk can extend the time and view code details.

## Slide 73: Guest Management Hotel Scenario(6/9)
However, our customer would like its staff to generate multiple accounts at once. How could that be achieved?

## Slide 74: Guest Management Hotel Scenario(7/9)

## Slide 75: Guest Management Hotel Scenario(8/9)
Use one of the codes to sig in the portal

## Slide 76: Guest Management Hotel Scenario(9/9)
After successful signing in, you are bring to the following message boxes.

## Slide 77: Guest Management
Usage scenario: coffee shop
Requirement:
  Shop clerks could generate and manage their guest Internet access codes.
  Policy: the code could be only used by one device and is valid for 2 hour. The shop clerk could extend the time per request.
Usage scenario: hotspot or business lobby
Requirement:
  Receptionists could generate and manage their guest Internet access codes and usage
  Policy: two types of codes will be issued:
    3-hour code
    100 MB code
    Users could consume time and traffic volume from multiple devices at the same time

## Slide 78: Guest Management Coffee Shop Scenario(1/2)

## Slide 79: Guest Management Coffee Shop Scenario(2/2)

## Slide 80: Guest Management Hotspot Scenario(1/9)
Usage by time

## Slide 81: Guest Management Hotspot Scenario(2/9)
Usage by traffic volume

## Slide 82: Guest Management Hotspot Scenario(3/9)
Verify the billing profiles you created

## Slide 83: Guest Management Hotspot Scenario(4/9)
Generate time-based codes.

## Slide 84: Guest Management Hotspot Scenario(5/9)

## Slide 85: Guest Management Hotspot Scenario(6/9)
Generate volume-based codes.

## Slide 86: Guest Management Hotspot Scenario(7/9)

## Slide 87: Guest Management Hotspot Scenario(8/9)
Sign in with a time-based code.
Observe from front desk management page.

## Slide 88: Guest Management Hotspot Scenario(9/9)
Sign in with a volume-based code.
Generate traffic and observe from front desk management page.

## Slide 89: Guest Management LAB
LAB time: 30 minutes
You need to practice the 3 Scenarios
Hotel
Coffee shop
Hotspot or lobby